## Slide 1
1 / 16
AARE · PSI HYBRID PIXEL DETECTORS · FEATURE/CUDA_CLUSTERFINDER
From 1.8 ms to 21 µs per frame
Eight optimization steps of the CUDA ClusterFinder — from the first kernel port (April 2026) to CUDA Graphs running over a fully pinned dataset (today).
×83
VS SINGLE-CORE CPU
×9.75
VS 48-THREAD CPU
47,747
FRAMES / SECOND
RTX 4090 (Ada, sm_89) · PCIe 4.0 ×16 · Mönch 400×400 uint16 · 3×3 clusters · Khalil Ferjaoui · July 2026

## Slide 2
2 / 16
THE PROBLEM & THE BASELINE
Where does a frame’s time go?
• Per pixel: subtract a running pedestal (mean ± rms), flag pixels above nσ · rms, extract a 3×3 cluster around each local maximum.
• 400×400 = 160k pixels, 312.5 kB / frame; Cu data yields ~1,300 clusters / frame.
• On the GPU, every frame pays three costs — and they color this whole talk:
one GPU frame
H2D copy
kernel
D2H + host API
compute
data movement
Thesis of this talk: the compute was fast almost immediately. Seven of the eight steps are really about feeding the GPU.
CPU, 1 THREAD
1.75 ms/frame
~570 FPS
CPU, 48 THREADS (MT)
204 µs/frame
~4,900 FPS

## Slide 3
3 / 16
STEP 0 · APRIL 2026 · COMMIT A438148
First CUDA port — one frame, one stream, fully synchronous
• Shared-memory tiling with generalized halo loading for any cluster size.
• Pedestal subtraction fused into the tile load.
• Compile-time cluster geometry → fully unrolled stencil reduction.
• Atomic global counter for lock-free cluster output across blocks.
// H2D → kernel → D2H, blocking, every frame
cudaMemcpy(d_frame, frame.data(), bytes, cudaMemcpyHostToDevice);
find_clusters_in_single_frame<<<grid, block, smem>>>(d_frame, d_ped, d_out);
cudaMemcpy(h_out, d_out, out_bytes, cudaMemcpyDeviceToHost);
~30× from the stencil alone — before any pipelining. This 57 µs is the “no batching, no overlap” floor every later step is measured against.
bench A · nσ=5
NOW
57 µs/frame
VS CPU 1-THREAD
×30 (1750 → 57)

## Slide 4
4 / 16
STEP 1 · COMMIT 3ED773E
Multi-stream scaffolding: find_clusters_batched()
• Each CUDA stream gets its own StreamContext: device frame, output and pedestal buffers.
• N frames distributed round-robin over n_streams.
• Host wrapper (.hpp) split from device kernel (.cuh).
struct StreamContext {
cudaStream_t stream;
FRAME_TYPE *d_frame;
ClusterType *d_clusters; uint32_t *d_cluster_count;
PEDESTAL_TYPE *d_pd_mean, *d_pd_sum, *d_pd_sum2;
};
std::vector<StreamContext> m_streams;
Scaffolding, not yet speed. “More streams = more overlap” only becomes true in Step 4, once the host stops synchronizing after every frame.
bench A · nσ=5
NOW (BATCHED, 1 STREAM)
52 µs/frame
STEP / TOTAL
−9% · ×33 vs CPU

## Slide 5
5 / 16
STEP 2 · COMMIT AC96D1F
Mixed precision: FP32 stencil, FP64 pedestal
• All stencil arithmetic and the shared-memory tile switch to float; pedestal accumulation stays double (for now — Step 5 finishes the job).
• Why: on Ada, FP32 throughput is ~64× FP64 — a sum/max/quadrant reduction needs none of that precision.
• The float tile (stride 18) maps to distinct shared-memory banks; the old double layout caused bank conflicts.
// clusterfinder_kernel.cuh
using COMPUTE_TYPE = float; // stencil + shared memory
auto load_pixel = [&] __device__ (ssize_t gr, ssize_t gc) -> COMPUTE_TYPE {
auto gid = gc + ncols * gr;
return static_cast<COMPUTE_TYPE>(d_frame[gid])
- static_cast<COMPUTE_TYPE>(d_pd_mean[gid]);
};
bench A · nσ=5
ISOLATED GAIN
no isolated benchmark —
prerequisite: pays out
as Step 5’s 3.3× kernel

## Slide 6
6 / 16
STEP 3 · COMMIT 34E69A8
Measure before optimizing: per-frame CUDA events
• Event pair around every kernel launch → avg_kernel_time_ms().
• Splits every number from here on into kernel vs PCIe + host overhead.
cudaEventRecord(m_kernel_start_pool[slot], stream);
find_clusters_in_single_frame<<<grid, block, smem, stream>>>(...);
cudaEventRecord(m_kernel_stop_pool[slot], stream);
// ...
cudaEventElapsedTime(&ms, start, stop);
Zero µs gained, and indispensable. Without this, Step 5’s 3.3× kernel speedup would be invisible — masked by PCIe in the wall-clock total.
bench A · nσ=5
PERFORMANCE CHANGE
±0
instrumentation only

## Slide 7
7 / 16
STEP 4 · COMMITS 88E0E8D + 6A12E3D
Remove the sync barriers, make transfers DMA-speed
• One cudaStreamSynchronize per stream per batch instead of one per frame: O(n_frames × n_streams) → O(n_streams) sync calls.
• Per-stream pinned staging buffers; caller’s batch pinned once via cudaHostRegister → ~22 GB/s instead of ~15 GB/s pageable.
• Unified D2H layout [count | clusters] in one lazily allocated pinned pool; sqrtf() thresholds → squared compares.
// continuous-queue launch loop — no per-frame sync
for (frame : frames_for_this_stream) {
cudaMemcpyAsync(sc.d_frame, ..., H2D, sc.stream);
find_clusters_in_single_frame<<<..., sc.stream>>>(...);
cudaMemcpyAsync(h_out_pinned[slot], ..., D2H, sc.stream);
}
for (auto &sc : m_streams) cudaStreamSynchronize(sc.stream); // once per stream
bench A · nσ=5
NOW (5 STREAMS)
28 µs/frame
THE PATH
52 → 34 → 28
1→5 streams, then
barriers removed (−18%)
VS CPU
×63

## Slide 8
8 / 16
HOW THE OVERLAP WORKS · THE MACHINERY BEHIND STEPS 4–6
Pipelining: per-frame cost = max of stages, not sum
1 STREAM, SYNCHRONOUS (STEP 0) — TIME → · EVERY ENGINE IDLE ⅔ OF THE TIME
one stream
H2D f0
krnl f0
D2H f0
H2D f1
krnl f1
D2H f1
5 STREAMS, ASYNC COPIES (STEP 4) — THE GPU’S THREE ENGINES RUN CONCURRENTLY
H2D copy engine
f0
f1
f2
f3
f4
f5
SM — kernel
f0
f1
f2
f3
f4
D2H copy engine
f0
f1
f2
f3
SAME INSTANT: f2 UPLOADS · f1 COMPUTES · f0 DOWNLOADS
What makes it legal: async DMA needs pinned host memory (pageable silently degrades to blocking), per-stream device buffers keep frames independent, and syncing once per stream keeps every queue full. The slowest stage — PCIe H2D, ~14 µs at 22 GB/s — now sets the frame rate; that is why every later step attacks transfers.
Step 6 adds a second overlap level: the CPU fills the next batch’s buffer while the GPU drains the current one.
bench A · nσ=5
1 STREAM, SERIAL
52 µs/frame
≈ Σ(H2D + krnl + D2H)
5 STREAMS, PIPELINED
28 µs/frame
≈ max(stage) + overhead

## Slide 9
9 / 16
STEP 5 · COMMIT 4C66802
FP32 device pedestal — a 3.3× kernel, a 7% frame
• Device pedestal arrays double → float (host master copy stays double); D2H drain becomes one resize + memcpy instead of per-cluster push_back.
• Kernel (CUDA events): 15 µs → 4.6 µs — but wall clock only moves 28 → 26 µs. The pipeline model says why:
BEFORE — PER-FRAME STEADY STATE, SHARED TIME SCALE · WALL 28 µS
H2D copy engine
312.5 kB · 14 µs
SM — kernel
kernel 15 µs
← pacing engine
AFTER — KERNEL FULLY HIDDEN INSIDE THE TRANSFER WINDOW · WALL 26 µS
H2D copy engine
312.5 kB · 14 µs
← pacing engine
SM — kernel
4.6
hidden — SMs idle rest of window
PCIe did not get slower — it just got exposed. Wall ≈ pacing engine + serial host overhead. Before, the SMs paced the pipeline by only 15 − 14 = 1 µs, so of the 10.4 µs kernel saving just ~2 µs sat on the critical path — the rest became SM idle time. The ~12 µs/frame of host work (launch, sync, drain) is untouched — exactly what Steps 7–8 attack.
bench A · nσ=5
NOW
26 µs/frame
KERNEL ONLY
15 → 4.6 µs (3.3×)
VS CPU
×67

## Slide 10
10 / 16
STEP 6 · COMMIT 5922C73
Async pipeline: hide the GPU inside the CPU’s memcpy
• submit_batch() enqueues H2D + kernel + D2H and returns a token — never blocks.
• collect() waits on a cudaEvent, not the stream — the next batch keeps running behind it.
auto tok = cf.submit_batch(buf_a, 0); // enqueue, don't wait
for (...) {
buf_b[:n] = data[start : start+n]; // CPU fills next buffer…
auto next = cf.submit_batch(buf_b, start);
results += cf.collect(tok); // …GPU chews meanwhile
tok = next; std::swap(buf_a, buf_b);
}
PER BATCH OF 2000 FRAMES (640 MB)
CPU staging memcpy · ~25 ms
GPU batch · ~12 ms
The CPU memcpy that fills the next buffer is longer than the GPU’s whole batch — so the GPU now runs entirely inside that window, for free.
bench A · nσ=5
NOW
22 µs/frame
STEP
26 → 22 (−15%)
VS CPU
×78

## Slide 11
11 / 16
STEP 7 · CURRENT BRANCH
Stop copying — pin the whole dataset where it lies
• The staging memcpy only exists because the pinned buffer was small. Invert it: cudaHostRegister the entire dataset in place — zero copies, submit raw slices.
• 6.1 GiB pinned for 20k frames; the 125 GiB node safely pins ~75 GiB ≈ 250k frames.
# pin once — no copy, just page-locking the existing buffer
cf.register_input_buffer(data)
for start in range(0, N, BATCH_SIZE):
results += cf.find_clusters_batched(data[start:stop], first_frame=start)
cf.unregister_input_buffer()
The best copy is no copy. Step 6’s pipeline carefully overlapped a memcpy that this step deletes — rerun on pinned data, the double-buffer path loses (44 µs/frame): its staging copy is now pure overhead.
bench B · nσ=7 · batch 5000
NOW
23.4 µs/frame
42,733 FPS
STEP (SAME BENCH)
94 → 23.4 µs
(×4.0 vs unpinned per-frame)
VS CPU 48-THREAD
×8.7

## Slide 12
12 / 16
STEP 8 · CURRENT BRANCH · CLUSTERFINDERCUDA_GRAPH.HPP
CUDA Graphs: record the pipeline once, launch it 20,000 times
• Per stream, the fixed chain memset → H2D → kernel → D2H is recorded into a cudaGraphExec once.
• Per frame, the host does only two pointer updates + one launch — instead of 3–4 full API calls with argument setup. At 40k+ FPS, host launch overhead is the tail that still matters.
// per frame: swap the two pointer-valued nodes, launch
sc.h2d_params.srcPtr = make_cudaPitchedPtr(h_src, ...);
cudaGraphExecMemcpyNodeSetParams(sc.graphExec, sc.h2d_node, &sc.h2d_params);
sc.d2h_params.dstPtr = make_cudaPitchedPtr(h_slot, ...);
cudaGraphExecMemcpyNodeSetParams(sc.graphExec, sc.d2h_node, &sc.d2h_params);
cudaGraphLaunch(sc.graphExec, sc.stream);
+12% on top of an already-pipelined path. Graphs rebuild lazily only when the pedestal syncs or the output pool resizes — steady state is pure launches.
bench B · nσ=7 · batch 5000
NOW
21.0 µs/frame
47,747 FPS
STEP
23.4 → 21.0 (×1.12)
VS CPU 48-THR / 1-THR
×9.75 / ≈×83

## Slide 13
13 / 16
VALIDATION · N = 20,000 FRAMES, CU FLUORESCENCE
Same physics out of every variant
• Cu spectra overlap across CPU and all three CUDA variants; ratio ≈ 1 through the photopeak.
• Stream and Graph variants agree exactly — 26,832,831 clusters each.
• GPU finds ~4.5% more clusters than CPU — expected: the GPU pedestal updates once per frame, the CPU per pixel, so thresholds diverge slightly over time.

## Slide 14
14 / 16
FOR USERS · PYTHON API
Using it from Python: pin, batch, collect
from aare import ClusterFinderCUDAGraph
cf = ClusterFinderCUDAGraph((400, 400), (3, 3), n_sigma=7,
max_clusters_per_frame=1500, n_streams=5)
for _ in range(1000): # train the pedestal
cf.push_pedestal_frame(f.read_frame())
cf.register_input_buffer(data) # pin in place — no copy
for start in range(0, N, BATCH_SIZE):
stop = min(start + BATCH_SIZE, N)
for cv in cf.find_clusters_batched(data[start:stop], first_frame=start):
hist.fill(cv.sum()) # one ClusterVector per frame
cf.unregister_input_buffer()
• Drop-in: same construction pattern and ClusterVector output as ClusterFinder / ClusterFinderMT — downstream analysis runs unchanged.
• One call, three engines: ClusterFinderCUDA (streamed) and ClusterFinderCUDAGraph (fastest) share the API; find_clusters(frame) covers the simple per-frame case.
• Pin once: register_input_buffer(data) page-locks the array in place — every slice then moves at DMA speed. Mind the pinning budget (available RAM − headroom; no swap).
• Advanced: submit_batch() / collect() overlap your own I/O or reduction with the GPU.
Results come back as one ClusterVector per frame with the frame number set — cv.sum(), histogramming and fitting code need no changes.

## Slide 15
15 / 16
THE JOURNEY IN TWO PICTURES
1.75 ms → 21 µs
CPU, 1 thread
1,750 µs
GPU, final (graphs + pinned)
21 µs ≈×83
ZOOM — GPU-ONLY STAGES, µS/FRAME (OWN SCALE)
0 · first port, sync
57
1 · batched, 1 stream
52
4 · 5 streams, no barriers, pinned staging
28
5 · FP32 pedestal
26
6 · async pipeline
22
7 · whole dataset pinned · bench B
23.4
8 · + CUDA graphs · bench B
21.0
Bench A (steps 0–6): nσ=5, vs single-thread CPU, recap benchmark. Bench B (hatched; steps 7–8): nσ=7, N=20k, batch 5000, notebook run — absolute values across benches are indicative, ordering within each bench is exact.
STAGE
µS/FRAME
FPS
VS 1-THREAD CPU
CPU reference
1,750
~570
×1
first CUDA port
57
~17,500
×30
streams + pinned staging + no barriers
28
~35,700
×63
+ FP32 pedestal · + async pipeline
22
~45,500
×78
whole-dataset pinning + CUDA graphs
21.0
47,747
≈×83

## Slide 16
16 / 16
WHAT’S NEXT
Every remaining lever is amber
• GPU-side cluster compaction before D2H — today D2H moves max_clusters_per_frame slots regardless of occupancy.
• Smaller Cluster struct — shrink the D2H payload per cluster.
• Larger batches — amortize the per-batch launch and sync overhead further.
• GPUDirect RDMA — delete H2D entirely when frames arrive over InfiniBand/RoCE, straight from the detector backend.
The kernel has been a 4.6 µs footnote since Step 5. The cluster finder is now a data-movement problem — and that is exactly where the next factor of two lives.
TODAY
21 µs/frame
47.7k FPS · RTX 4090